## Slide 1: Wind Powered Water Pump Project Team 1
B. Lars, D. Oran, J. Prat, M. Fiat I. Urog

## Slide 2: Problem Statement
OBJECTIVE: Design and engineer a simple wind powered water pump within a budget constraint for the people in need in Congo, which have a hard access to clean water.
TARGET REGION:
Democratic Republic of the Congo
Household income: $395 per year
Primary customers: end users
Secondary customers: entrepreneurs

## Slide 3: Voice of the Customer
CUSTOMER NEEDS:
Affordable (9)
Water pumped over time (9)
Quality of product (durability) (9)
Ease of use (3)
Ease of maintenance (3)
Ease to assemble (1)
Aesthetics (1)

## Slide 4: Specifications and Benchmarking
SPECIFICATIONS
Easy to setup and repair
It is able to power the product at 5 m/s wind speed
Product is made with durable and long-lasting materials
Tank holds 50 liters of water
Cost less than $100
Locally/Recycled stored materials are used in fabrication
COMPETITION
Johnson & Johnson
OakenHurst
Global Water Initiative
Practical Action

## Slide 5: Engineering Model

## Slide 6: Concept Selection

## Slide 7: Prototype Design and Fabrication
KEY CHALLENGES IN FABRICATION:
Attaching the camshaft to the pump assembly

## Slide 8: Prototype Testing
Test | Calculated result | Tested result | Conclusion
Does it pump? | It pumps | It does not pump | FAIL, pump does not work horizontally
Minimum wind speed | 2.74 m/s | 9.17 m/s | FAIL, friction and resistance were not included
Wind speed to revolutions per second | 2.64 m/s | 8.84 rps | FAIL, the results are inconsistent

## Slide 9: Profitability Analysis
3-year plan: 25,000 units, increasing by 10% after every year
$74 per unit, increasing $1 per year due to inflation
Market price: range between $2,000 to $15,000, depending on the quality of the product
Break even point: after 8,110 units
Each unit costs less than $70

## Slide 10: Final Design Concept
Testing revealed:
Too much friction
The pump does not work horizontally
Changes:
Washers were added between connector and cam
Did not use tubing
Made the hole on the cam closer to the middle for less range of motion

## Slide 11: Concluding Thoughts
Challenges:
Reducing friction in the cam mechanism
Attaching the pump
File organization system
Pump selection