## Slide 1: Engineering Capstone: Construction Estimating Overview
The following slides will provide a brief overview of the material and equations covered during the Construction Estimating course.
Elissa Ledoux
M. Moin Uddin
Nicholas Matta
Matthew Sheppard

## Slide 2: Four Stages of the Estimating Process:
Planning the bid
Pre-bid day activities
Bid-day activities
Post-bid activities

## Slide 3: Steps for Preparing Detailed Estimates:
Planning the bid:
Define scope of work.
Schedule the bid.
Assign tasks.
Pre-bid activities:
Order bond.
Request subcontractor quotes.
Perform quantity takeoff (material, labor, equipment prices).
Calculate project overhead.
Prepare bid document.
Bid day activities:
Select subcontractors.
Combine pricing.
Add markups.
Review bid for errors.
Submit bid.
Post bid activities:
Review bid.
Project buyout.
Close-out audit.

## Slide 4: Taking Phone Quotes:
Collect project details, subcontractor contact information, bid items, and specifics like addends, inclusions, exclusions, sales tax, and freight.

## Slide 5: Fundamentals of Quantity Takeoff
Quantity Takeoff
  The process of preparing a complete list of all building components needed for a project, also known as a quantity survey.
  Examples include footings, masonry walls, windows, and jobsite overheads like supervision and temporary facilities.

## Slide 6: Categories of Materials for Quantity Takeoff
Counted Items: Nonrepetitive and repetitive items.
Linear Items: Measured by length (e.g., footing forms, rebar for continuous footings).
Sheet and Roll Goods: Measured by area (e.g., wall forms, face brick).
Volumetric Goods: Measured by volume (e.g., concrete, excavation).
Quantity-from-Quantity Goods: Estimated based on the quantity of another item (e.g., paint, roofing nails).

## Slide 7: Commonly Used Units
Linear feet, square feet, board feet, square yards, cubic yards, acres, each, months, lump sum.
Conversion Factors
1 yard = 3 feet
1 square yard = 9 square feet
1 cubic yard = 27 cubic feet
1 foot = 12 inches

## Slide 8: Methods for Calculating Quantities
Repetitive Counted Items: Use mathematical equations for items at both ends, one end, or neither end.
  (D) = distance over which the item occurs
  (S) = spacing between the items
  Ensure both spacing and distance are measured in the same unit
Repetitive Item at Both Ends
  Number of Items + 1
Repetitive Item at One End
  Number of items
Repetitive Item at Neither End
  Number of Items - 1

## Slide 9: Linear Components
Calculate based on length, considering butt joints and lap joints.
  Measured by length
  Common units: linear feet (feet), each
  Examples: footing forms, rebar for continuous footings, steel handrails, fencing, etc.
  Number of Pieces: Number of Pieces =
  (L) = Length of linear component
  (Le) = Effective length = distance between the start of the pieces
    Butt Joint: no overlapping
      Le – length of a piece (Lp)
      Number of pieces =
    Lap Joint: overlapping
      Le = length of piece (Lp) – Lap
      Number of pieces =

## Slide 10: Sheet and Roll Goods
Use area method or row and column method, considering butt joints, lapped joints, and spaced joints.
𝑁𝑢𝑚𝑏𝑒𝑟 𝑜𝑓 𝑝𝑖𝑒𝑐𝑒𝑠 =
L = Area to be covered
Ae = Area covered by one piece including spacing or lap
  Butt Joint:
    No overlapping, no spacing
    Ae = Length x Width
  Lapped Joint:
    Overlapping
    Ae = (Length – LapLength) x (Width – Lapwidth)
  Spaced Joints:
    Spacing between the pieces
    Ae = (Length + SpaceLength) x (Width + SpaceWidth)

## Slide 11: Row and Column Method
Number (N) = Number of rows (Nrows) x (Ncolumns)
  Butt Joint:
    Nrows =
    Ncolumns =
  Lapped Joint:
    Nrows =
    Ncolumns =
  Spaced Joints:
    Nrows =
    Ncolumns =

## Slide 12: Volumetric Goods
Calculate volume for different shapes like cylinders, columns, prisms, cones, and pyramids.
  Rectangular column: Height x Width x Length
  VCylinder = πR2H
  VColumn = LWH
  VPrism = BHL/2
  VCone = πR2H/3
  VPyramid = LWH/3

## Slide 13: Quantity-from-Quantity Goods
Use coverage-based or average quantity-based methods.
  Quantity = Quantity of material needed
Coverage Based:
  Quantity =
    Quantitybase= Quantity of the item that the estimate is based upon
    Coverage = coverage of the material needed
Average Quantity Based:
  Quantity = Quantitybase x Average Quantity required
    Quantitybase= Quantity of the item that the estimate is based upon
    Average Quantity required = Average quantity needed to cover one unit of base material

## Slide 14: Waste Management
Avoidable Waste: Due to improper use, lost or damaged materials, and discrepancies between actual and design dimensions.
Unavoidable Waste: Resulting from the inability to use scrap materials.
Formula for calculating waste:
  Quantitywith waste = Quantity without waste(1 +
  Waste percentage can be obtained from the historical data or experience

## Slide 15: Concrete
Components of Concrete Works
  Forms: Measured in square feet, linear feet, or sets. Include all sides.
  Reinforcing: Includes rebar, rebar chairs, welded wire fabric (WWF), and wire ties.
  Concrete: Consider admixtures, weather, and waste (typically 5-10%).

## Slide 16: Specific Concrete Elements
Spot (Column) Footings:
  Concrete is a volumetric good (Volume = Height × Width × Length).
  Forms are linear or sheet goods depending on height.
  Rebar and dowels are counted items.
Columns:
  Rectangular: Concrete is volumetric, forms are linear/sheet goods, rebar and ties are counted.
  Round: Concrete volume calculated using:
  π (Diameter/2)² × Height.
Continuous Footings:
  Concrete is volumetric.
  Forms are linear or sheet goods.
  Rebar includes cross bars, dowels (counted items), and continuous bars (linear goods).

## Slide 17: Specific Concrete Elements Cont.
Foundation Walls:
  Concrete is volumetric.
  Forms are sheet goods.
  Rebar includes vertical (counted) and horizontal (linear) rebar.
Beams:
  Estimated similarly to walls but include forms on the bottom and specialty rebar like stirrups.
Slab on Grade:
  Estimated similarly to walls but include forms on the bottom and calculate the area to be finished.
Raised Slabs:
  Concrete is volumetric (Volume = Width × Length × Average Thickness).
    Average Thickness (Tave)
    Tave = T + (W1 + W2)D/(2S)
Stairs:
  Concrete is volumetric (Volume = Cross Section × Width).

## Slide 18: Masonry
Blocks and Structural Brick
  Block and Structural Brick: Considered sheet goods.
  Vertical Rebar and Rebar Around Openings: Counted items.
  Horizontal Rebar: Linear good.
  Mortar and Grout: Quantity-from-quantity goods, based on past experience.
  Anchor Bolts and Embeds: Counted items.

## Slide 19: Brick Veneer
Brick: Considered a sheet good.
Brick Ties: Counted items, needed at the top and corners of walls.
  Number of Rows = Height / Spacing
  Number of Columns = Length / Spacing + 1
  Ties = NumberRows × NumberColumns
Mortar: Volumetric good, based on past experience.

## Slide 20: Metals
Steel Shapes:
Understanding different steel shapes used in construction.
Weight of Beams and Columns:
Calculating weight using the formula:
Weight = Length × Weight Per Length
Approximate weight is 490 lb/cubic foot.
Connections:
Various types of beam and column connections:
Beam to beam – measure to the center of the beam
Beam to column flange – measure to the column flange
Beam over top of the column – measure across the column
Joists:
Joists are counted items.
Designation and specifications for joists. 24K3 (depth/joist type/section#)
Joist Girders:
Joist girders are also counted items.
Designation and specifications for joist girders. 24G5N8K (depth/girder/# of spaces/Load on each panel point)
Metal Deck:
Metal deck is considered a sheet good.
Trusses and Handrails:
Listing components including welding and bolts.

## Slide 21: Woods, Plastics, and Composites
Floor Systems:
  Sills: Linear component, must be durable or pressure-treated wood.
  Posts, Girders, Joists: Counted items.
  Rim Joists, Blocking: Linear components.
  Floor Sheathing, Wood Decking: Sheet goods.
  Openings: Require doubled trimmers and framing anchors for larger openings.

## Slide 22: Walls
Top and Bottom Plates: Linear goods.
Studs: Counted items, with extra studs needed at corners, intersections, and openings.
Headers: Counted items, may require plywood spacers.
Hold Downs, Blocking: Counted and linear components respectively.
Wall Sheathing: Sheet good.

## Slide 23: Roof Systems
Rafters, Trusses: Counted item
  Common rafter:
    Length = (Run2 + Rise2)0.5 + Width (Rise/Run)
    Length = Run (1 + Slope2)0.5 + Width(Slope)
Roof Sheathing: Sheet good.
  Hip rafter:
    Length = RunCommon(2 + SlopeCommon2)0.5 + Width(SlopeHip)
Fascia: Linear good.
  WidthFascia= WidthRafter(1 + Slope2)0.5 + ThicknessFascia(Slope)
Soffit: Sheet good.

## Slide 24: Finish Carpentry and Cabinets
Trim, Shelving, Cabinets: Counted items.
Paneling: Sheet good

## Slide 25: Thermal and Moisture Protection
Shingle Roofs:
Drip Edge: Installed around the perimeter of the roof, considered a linear component.
  Field Shingles: Calculations involve the slope of the roof and average width of trapezoid.
    Starter
      Areastarter shingles = Exposure (ft) * Length (ft)
    Standard
      Areastandard shingles for field= Areaplan(ft2) *
        s = slope of roof
    Cap
      𝐴𝑟𝑒𝑎𝑐𝑎𝑝 𝑠ℎ𝑖𝑛𝑔𝑙𝑒𝑠 𝑓𝑜𝑟 𝑟𝑖𝑑𝑔𝑒 = 𝐿𝑒𝑛𝑔𝑡ℎ𝑟𝑖𝑑𝑔𝑒 ∗ 1𝑓𝑡
      𝐴𝑟𝑒𝑎𝑐𝑎𝑝 𝑠ℎ𝑖𝑛𝑔𝑙𝑒𝑠 𝑓𝑜𝑟 ℎ𝑖𝑝 = 𝐿𝑒𝑛𝑔𝑡ℎ𝐻𝑖𝑝 𝑖𝑛 𝑝𝑙𝑎𝑛 ∗ ∗ 1𝑓𝑡
        sh = slope of hip

## Slide 26: Thermal and Moisture Protection Cont.
Building Paper and Vapor Barriers:
  Calculations include the slope of the roof and additional areas for hip/valley in hip roofs.
    Lengthsloped = Lengthplan *
      S = slope of roof
    Average width of trapezoid
      = (W1+W2)/2 + Wfelt + LapEnd
      LengthRidge felt = LengthRidge + 2*LapEnd

## Slide 27: Thermal and Moisture Protection Cont.
Vinyl or Aluminum Siding:
  Components: Starter strip, outside corner molding, J molding (around openings and at soffit), and siding.
  Starter Strip, Corner Molding, and J Molding: Linear components.
  Siding: Considered a sheet good. Trapezoidal or triangular portions are approximated by calculating the average length.
    Vinyl or Aluminum Siding:
      𝐿𝑒𝑛𝑔𝑡ℎ = +

## Slide 28: Earthwork
Characteristics of Soils
Wet Unit Weight (Wet Density): Density of water and solids.
Dry Unit Weight (Dry Density): Density of the solids.
Water Content: Ratio of the weight of water to the weight of solids.
Swell and Shrinkage
Swell Percentage: Soils increase in volume when excavated.
Swell % = (DB/DL – 1)100
DB = Bank dry density (unit weight)
DL = Loose-dry density (unit weight)
Shirkage Percentage: Soils decrease in volume as they are compacted.
Shrinkage % = (1 - DB/DC)100
DB = Bank dry density (unit weight)
DC = Compact dry density (unit weight)

## Slide 29: Geometric Methods
Average-width-length-depth Method
  Volume = (Wave)(Lave)(Dave)
    Wave= average width
    Lave= average depth
    Dave= average depth at bottom of excavation (does not include side slopes)

## Slide 30: Average End Method
Volume = L(A1 + A 2)/2
L = perpendicular distance between the cross-sections
A1 = Area of cross-section 1
A2 = Area of cross-section 2
Volume = L(0.5A1 + A2 + A3 + … + An-1 + 0.5An)
L = Perpendicular distance between the cross sections (must be the same for all cross sections)
A1 = Area of cross-section 1
A2 = Area of cross-section 2
A3 = Area of cross-section 3
An-1 = Area of cross-section n-1
An = Area of cross-section n

## Slide 31: Modified-Average-end Method
  Volume = L[A1 + A 2 + ]/3
    L = Perpendicular distance between the cross-sections
    A1 = Area of cross section 1
    A2 = Area of cross section 2

## Slide 32: Cross Sectional Method
Cross Sectional Method:
  Step 1: Divide the site into grids
    Equally spaced
    Aligned with key features
  Step 2: Calculate the cut or fill at each grid intersection
    Cut/Fill = GradeProposed – GradeExisting
      Positive = Fill
      Negative = Cut

## Slide 33: Cross-Sectional Method cont.
  Step 3: If existing grade is not known at a grid intersection, it can be calculated by interpolating
    GradeP = (Grade2 – Grade1 )(DistP-1 )/(Dist2-1 ) + Grade1
      GradeP = Grade at intersection
      Grade1 = Grade of first contour line
      Grade2 = Grade of second contour line
      DistP-1 = Distance between the intersection and first contour line
      Dist2-1 = Distance between the second and first contour line

## Slide 34: Cross Sectional Method cont.
Step 4: Separate the cuts and fills with a zero line
  DistC-0 = (DistC-F )(Cut)/(Cut + Fill)
    DistC-0 = Distance from the intersection with a cut to the zero Line
    DistC-F = Distance from the intersection with a cut to the intersection with a fill
    Cut = Cut at the intersection with a cut (use a positive sign)
    Fill = Fill at the intersection with a fill (use a positive sign)
Step 5: Calculate the volume of the cuts and fills
  Cuts and fills calculated separately
  VolumeCut = (CutAverage)(AreaCut)
    CutAverage = ∑Cut/Number of cuts
  VolumeFill = (FillAverage)(AreaFill)
    FillAverage = ∑Fill/Number of fills
  Area = rectangular or triangular areas
  Total Volume of cuts and fills

## Slide 35: Backfill Volume
VBackfill = VExcavation – VFooting – VColumn
  VColumn = Volume of the column below ground level excluding the footing depth